## Slide 1: Go for rsync Diversity
Simon Leinen <simon.leinen@switch.ch>, Switch (AS559)
RIPE 90 Routing WG, 15 May 2025

## Slide 2: Management Summary
I tried to use Michael Stapelberg1’s “gokrazy” rsync variant for fetching RPKI material (ROAs) with Routinator and FORT.
It works2
RRDP is still the better protocol, ceterum censeo rsync delendum esse(???)
  1 He did all the work. Thank you, Michael! 2 For some value of “works”With a bit of configuration fiddling, reliably with acceptable performance, and (small) manageability impact
TL;DL

## Slide 3: Diversity for RPKI Robustness
Many operators use different RPKI caches/validators, e.g. two of
  Routinator 3000
  rpki-client
  FORT
Should we use different rsync implementations as well?
  (Assumption: We still need rsync at all until everyone has moved to RRDP)

## Slide 4: Rsync variants
“Tridge” rsync
openrsync (in OpenBSD and macOS(?))
Gokrazy rsync
  Written from scratch/spec in Go, a memory-safe language
  By Michael Stapelberg (of router7 fame)
(possibly others, not all well supported anymore)

## Slide 5: Why Go?
“Memory safe”, i.e. no buffer overflows and use-after-free
  Remember CVE-2024-12084 & friends?
Easy multithreading model, useful for networking tools

## Slide 6: Why “gokrazy” rsync?
Michael has large-systems and Go “street credibility”
He expressed willingness to help with this use case (implement missing options etc.)
We live in the same town country

## Slide 7: gokr-rsync compatibility status
rpki-client: Assumes support for (too) many rsync options
FORT: works, as of May 2025—see below
Routinator 3000: works, as of March 2025
rsync-command = "/usr/bin/gokr-rsync"
rsync-args = ["--compress", "--no-motd", "--contimeout=10"]
/etc/routinator/routinator.conf:

## Slide 8: Measurement results
FORT 1.6.6, rsync.priority=90 (prefer rsync over RRDP)
 | Tridge rsync | gokr-rsync
Initial load time | ~980s (16’20”) | ~1600s (26’40”)
Subsequent refresh times | ~823–1’001s | ~751–986s
#Validated ROAs after initial load | 687’868 | 693’054
#Validated ROAs over a few hours | 687’868–693’075 | 692’863–693’079

## Slide 9: Possible Future Work
Add missing command-line args (--include/--exclude etc.)
Maybe add diverse return codes like Tridge rsync
Use as library for Go-based RPKI implementations?

## Slide 10: BUT WHY?
Haven’t we moved past rsync for RPKI?
RRDP is the future! (Or we’ll come up with something else…)
Yes, but…
  Even when deprecated, we’ll have to support rsync for RPKI for “a while” (years)
  Keeping old infrastructure running—not sexy but someone has to do it (to enable blockchain, AI…)
(OK, the actual reason was that I wanted to learn Go from the pros… ;-)