## Slide 1
Annet takes control
of the network
Grigorii Solovev, Yandex Infrastructure | RIPE 90 | 13.05.2025

## Slide 2
Annet - network configuration automation tool
Grigorii Solovev | RIPE 90 | 13.05.2025
Opensource project - https://github.com/annetutil
Widely adopted in several large companies
Supports vendors:
Cisco – Cisco IOS/-XE/-XR, NXOS
Juniper – JunOS
Huawei – VRP5/VRP8
Arista – EOS
Nokia – TiMOS
MikroTik – RouterOS
SONiC – /etc/sonic/config_db.json
Whitebox – Linux (FRR, snmpd, ntpd and etc)

## Slide 3
Why we decided to develop Annet?
Grigorii Solovev | RIPE 90 | 13.05.2025
Multivendor networks
Legacy devices
A lot of devices in production (10k+)
Complicated configurations
Transition between configurations

## Slide 4
Software defined configuration
Grigorii Solovev | RIPE 90 | 13.05.2025
Full configuration templating
Create reference configuration and deploy it
Advantages:
  Configuration checks
  Mass changes
  Actual documentation
  Git, review and tests

## Slide 5
Configuration methods
Grigorii Solovev | RIPE 90 | 13.05.2025
Requirements | CLI | NETCONF | Ansible
Machine-readable |  |  | 
Multivendor |  |  | 
Reliable delivery |  |  | 
Human-readable |  |  | 
Comfortable for writing |  |  | 
Versatility |  |  | 

## Slide 6
Annet uses CLI method
Grigorii Solovev | RIPE 90 | 13.05.2025
Every device has CLI
CLI is convenient for engineers
CLI is machine-readable in reality
Need to be solved:
Multivendor support
Reliable delivery

## Slide 7
Annet: fundamental
Grigorii Solovev | RIPE 90 | 13.05.2025
Declarative
Modularity
Templates on Python
Can support every device (every device has CLI)
There is no one single model of device configuration
Integrated with inventory system
Server less, only CLI client

## Slide 8
Hands on examples
Grigorii Solovev | RIPE 90 | 13.05.2025
ntp server disable
ntp ipv6 server disable
ntp server source-interface all disable
ntp ipv6 server source-interface all disable
ntp unicast-server 95.108.129.181 vpn-instance MEth0/0/0
ntp unicast-server 95.108.129.183 vpn-instance MEth0/0/0
ntp unicast-server 37.140.149.198 vpn-instance MEth0/0/0
clock timezone UTC add 00:00:00
$ annet gen –g ntp sas-127d2

## Slide 9
Hands on examples
Grigorii Solovev | RIPE 90 | 13.05.2025
$ annet diff –g ntp sas-127d2
- clock timezone FRA add 02:00:00
+ clock timezone UTC add 00:00:00
+ ntp unicast-server 95.108.129.181 vpn-instance MEth0/0/0
+ ntp unicast-server 95.108.129.183 vpn-instance MEth0/0/0
$ annet patch –g ntp sas-127d2
ntp unicast-server 37.140.149.198 vpn-instance MEth0/0/0
ntp unicast-server 37.140.149.199 vpn-instance MEth0/0/0
clock timezone UTC add 00:00:00
$ annet deploy –g ntp sas-127d2
$

## Slide 10
Architecture
Grigorii Solovev | RIPE 90 | 13.05.2025
Inventory
…
YAML
NetBox
Models
…
Device
RPL
Mesh
Generators
…
SNMP
NTP
BGP
Golden configuration
Device configuration
Diff
Rulebook
rul
order
deploy
patch
deploy

## Slide 11
Models: Device
Grigorii Solovev | RIPE 90 | 13.05.2025
Based on inventory data
Create python class object
>>> device.fqdn
'sas-127d2.yndx.net’
>>> bool(device.hw.Arista)
False
>>> [iface.name for iface in device.interfaces]
['10GE1/0/1', '10GE1/0/2', …, 'Eth-Trunk217’, 'Eth-Trunk218', …, 'LoopBack0', 'MEth0/0/0']

## Slide 12
Models: RPL
Grigorii Solovev | RIPE 90 | 13.05.2025
Route policies are described in Python pseudo code
Create python class objects
@routemap def IMPORT_CONNECTED(device, route): with route( number=10, R.protocol == "connected", R.match_v4("LOCAL_NETS", or_longer=(24, 32)) ) as rule: rule.community.set("ADVERTISE") rule.allow() with route(number=20) as rule: rule.deny()

## Slide 13
Models: RPL
Grigorii Solovev | RIPE 90 | 13.05.2025
Route policies elements are defined by Python objects
PREFIX_LISTS = [ IpPrefixList(name="LOCAL_NETS", members=["192.168.0.0/16"]) ]
COMMUNITIES = [ CommunityList(name="ADVERTISE", members=["65000:1"]) ]

## Slide 14
Models: Mesh
Grigorii Solovev | RIPE 90 | 13.05.2025
Describe device neighbors based on templates
Templates applies to connection in the inventory
Create Python class objects for remote peers
@registry.direct("tor-{pod}-{num}", "spine-{pod}-{plane}")
def tor_to_spine(tor, spine, session):
tor.asnum = BASE_ASNUM + 100 + tor.match.pod * 10 + tor.match.num
tor.addr = f"10.{spine.match.plane}.{tor.match.num}.12/24"
tor.import_policy = "TOR_IMPORT_SPINE"
tor.export_policy = "TOR_EXPORT_SPINE"
spine.asnum = BASE_ASNUM + 200 + spine.match.pod
spine.addr = f"10.{spine.match.plane}.{tor.match.num}.11/24"
spine.import_policy = "SPINE_IMPORT_TOR"
spine.export_policy = "SPINE_EXPORT_TOR"

## Slide 15
Models: Mesh
Grigorii Solovev | RIPE 90 | 13.05.2025
>>> [(peer.addr, peer.remote_as) for peer in mesh_data.peers]
[('10.1.1.11', ASN(65201)), ('10.2.1.11', ASN(65201))]

## Slide 16
Generator
Grigorii Solovev | RIPE 90 | 13.05.2025
Python generator is class with per vendor methods
Generators has access to inventory data and models
It yields configuration lines
def run_juniper(self, device):
if device.tags[”Frankfurt"]:
servers = NTP_SERVERS_FRA
else:
servers = NTP_SERVERS_GLOBAL
for server in servers:
with self.multiblock("system", "ntp"):
yield "server", server, "version 3"
def run_huawei(self, device):
if device.tags[”Frankfurt"]:
servers = NTP_SERVERS_FRA
else:
servers = NTP_SERVERS_GLOBAL
for server in servers:
yield "ntp unicast-server", server

## Slide 17
ACL
Grigorii Solovev | RIPE 90 | 13.05.2025
Limit scope of the generator
Limit configurations lines for diff
Uses for modularity
snmp-agent
ifindex constant
interface
mac-address trap notification
mac-address notification learning
set if-mib discard-statistics enable
acl number 410
acl ipv6 number 610

## Slide 18
Rulebook
Grigorii Solovev | RIPE 90 | 13.05.2025
Redefine no/undo/delete commands to expected format
Very flexible logic
Order of configurations lines in patch
Response on questions
interface 100GE0/1/39 - port-queue ef wfq weight 3 outbound + port-queue ef wfq weight 5 outbound
interface 100GE0/1/39 undo port-queue ef wfq outbound port-queue ef wfq weight 5 outbound quit

## Slide 19
Deploy
Grigorii Solovev | RIPE 90 | 13.05.2025
Opensource library - gnetcli
Written on Golang
Annet uses gnetcli for connection to devices

## Slide 20
gnetcli
Grigorii Solovev | RIPE 90 | 13.05.2025
Pagination
Interactive interaction
NETCONF
Various network operating systems
CLI tool
GRPC server
Python SDK

## Slide 21
Real world example - drain spine in DC fabric
Grigorii Solovev | RIPE 90 | 13.05.2025
Assign tag to the device
Update route policy
$ annet diff –g rpl spine-1-1
route-map SPINE_EXPORT_TOR permit 10
+ set community 65535:0 additive
$ annet deploy –g rpl spine-1-1
$
The task is done

## Slide 22
Real world example - drain link between devices
Grigorii Solovev | RIPE 90 | 13.05.2025
Assign tag to the cable
Update bgp configuration
$ annet diff –g bgp r1
router bgp 65001
+ neighbor 10.1.2.12 shutdown
$ annet deploy –g bgp r1
$
The task is done

## Slide 23
Annet – feel free to add new ones
Grigorii Solovev | RIPE 90 | 13.05.2025
Supports vendors:
Cisco – Cisco IOS/-XE/-XR, NXOS
Juniper – JunOS
Huawei – VRP5/VRP8
Arista – EOS
Nokia – TiMOS
MikroTik – RouterOS
SONiC – /etc/sonic/config_db.json
Whitebox – Linux (FRR, snmpd, ntpd and etc)

## Slide 24
Annet – how to try
Grigorii Solovev | RIPE 90 | 13.05.2025
Project repository - https://github.com/annetutil
Tutorial
Labs
Telegram chat

## Slide 25
Grigorii Solovev | RIPE 90 | 13.05.2025